## Slide 1
Digital Decibel Sound Level Indicator with Peak-Hold
A register-level design in VHDL
Computer Organization & Architecture (BTS30101)
Sayantan Bharati | BWU/BTS/25/503 | Section B
B.Tech CSE, Batch 2025 | Faculty: Dr. Subhankar Shome
Brainware University | 03-11-2026
Notes: Good morning. My project is a digital sound level meter with peak-hold, written in VHDL. This presentation focuses on the digital design only: the entity, the registers, the comparator and the testbench.

## Slide 2
Where the Design Starts
The analog world ends at one 8-bit bus
Mic, amp, filter, ADC
analog, abstracted
din[7:0]
sound_meter
VHDL, clocked
db[7:0]
peak[7:0]
Assume
The ADC hands the design one 8-bit unsigned sample per clock.
Study
Entity, registers, comparator, synchronous reset, testbench.
Skip
Microphone, amplifier and ADC circuit. Not part of this design.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 2
Notes: This is the only non-digital slide. The microphone, amplifier and ADC are abstracted into one box. From the din bus onward, everything is VHDL and register-level design.

## Slide 3
The Interface: Entity
Five ports define the whole design
entity sound_meter is
Port (
clk : in STD_LOGIC;
rst : in STD_LOGIC;
din : in STD_LOGIC_VECTOR(7 downto 0);
db : out STD_LOGIC_VECTOR(7 downto 0);
peak : out STD_LOGIC_VECTOR(7 downto 0)
);
end sound_meter;
clk
in
1 bit
rst
in
1 bit
din
in
8 bit
db
out
8 bit
peak
out
8 bit
8-bit data width: values 0 to 255.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 3
Notes: The entity is the hardware boundary. A clock, a reset and an 8-bit sample come in. Two 8-bit values go out: the registered sample and the held peak.

## Slide 4
Datapath View
Two registers and one comparator
din
d
variable
db reg
db
d > p ?
p reg
peak
feedback of p
No arithmetic beyond one compare. The peak is simply the largest value p has stored so far.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 4
Notes: Read it as hardware. The sample is captured into a variable d. It goes straight to the db register. In parallel, a comparator checks d against p, and p is the register that remembers the peak, fed back into the comparator.

## Slide 5
Clocked Process and Reset
Everything happens on the rising clock edge
process(clk)
variable d : unsigned(7 downto 0);
begin
if rising_edge(clk) then
if rst = '1' then
db <= (others => '0');
peak <= (others => '0');
p <= (others => '0');
else
-- datapath (next slide)
end if;
end if;
end process;
Edge-triggered
rising_edge(clk): flip-flops.
Synchronous
rst is read only at a clock edge.
Reset state
db, peak, p all become 0.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 5
Notes: The whole design lives in one clocked process. The reset is checked inside the clock edge, so it is synchronous. Reset forces both outputs and the internal peak register to zero.

## Slide 6
Peak-Hold: Compare and Store
The core of the design in three lines
d := unsigned(din);
db <= std_logic_vector(d);
if d > p then
p <= d;
end if;
peak <= std_logic_vector(p);
d > p
New maximum. Store it in p.
d <= p
No branch taken. p keeps its old value.
p never decreases, except through reset. That is what makes it a hold.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 6
Notes: This is the peak-hold. If the new sample is larger than the stored one, overwrite it. Otherwise the register keeps its value. Nothing else is needed, and p can only go down through reset.

## Slide 7
Variable vs Signal
Why peak trails by one clock
variable d :=
Updates immediately. Used for db and the compare in the same edge.
signal p <=
Updates after the edge. peak reads the old p.
Testbench instant: din changes from 10 to 30
edge at 125 ns
edge at 135 ns
din
30
30
p
30
30
peak
10
30
peak = p delayed one clock. db = din delayed one clock.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 7
Notes: This is the one subtle point in the code. d is a variable, so it updates immediately. p is a signal, so peak sees the old value of p. The table shows it: at 125 ns p becomes 30 but peak still shows 10. One clock later peak shows 30.

## Slide 8
Testbench Structure
Instantiate, clock, reset, stimulate
uut: entity work.sound_meter
port map (clk => clk, rst => rst,
din => din, db => db,
peak => peak);
clk <= not clk after 5 ns;
rst <= '1'; wait for 20 ns;
rst <= '0';
din <= x"10"; wait for 100 ns;
din <= x"30"; wait for 100 ns;
-- ... x"A0", x"20", x"00"
Clock
10 ns period, toggles every 5 ns.
Reset
20 ns at start, 30 ns mid-run.
Stimulus
10 values, 100 ns each.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 8
Notes: The testbench has no ports. It instantiates the design, generates a 10 nanosecond clock, applies reset, then drives ten sample values for 100 nanoseconds each, with a second reset in the middle of the run.

## Slide 9
Simulation Results
Settled value at the end of each 100 ns step
din
peak
10
10
30
30
50
50
70
70
90
90
60
90
40
90
A0
A0
20
A0
00
A0
R
00
80
80
R = rst asserted. Green cells show the peak changing.
Ignored
60 and 40 arrive after 90. peak stays at 90.
New max
A0 beats 90. peak moves up, then 20 and 00 are ignored.
Reset
rst clears peak to 00. Then 80 starts a new hold.
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 9
Notes: Read the two rows. The sample values go up to 90, then drop to 60 and 40, and the peak stays at 90. A0 raises the peak. The reset clears it to zero, and the next sample, 80, starts a new peak.

## Slide 10
COA Concepts and Next Steps
What this small design demonstrates
In this design
Registers (p, db)
Comparator and feedback
Clocked sequential logic
Synchronous reset
Not yet in the code
Log (dB) conversion: db is the raw sample
RMS windowing
Hold timer or decay
Thank you.
Refs: Patterson & Hennessy; Stallings; Hamacher
Complete Code(Github): Click here
Sayantan Bharati | BWU/BTS/25/503 | Section B | COA (BTS30101) | 10
Notes: To summarise: registers, a comparator, clocked logic and a synchronous reset are enough to build a working peak-hold. The natural next steps are a log lookup table for true decibel output and a hold timer. Thank you.